## Slide 1: Side Channel Attacks Against the Arduino Uno Owen Lo Edinburgh Napier University

## Slide 2: Presentation Outline
Introduction to Side Channel Attacks
Timing Attack Demo
SPA/DPA/CPA Power Analysis Overview
  DPA/CPA attacks against the AES-128 S-Box on an Arduino Uno

## Slide 3: Side Channel Attacks
Plaintext
Message
Encrypted
Message
Cryptographic Function
Secret Key
Power
Heat
Time
Sound
Side Channel Monitoring
A side channel attack is carried out by monitoring the physical outputs of a device (e.g. power consumption, time taken to carry out an operation, emission of heat, light and sound).

## Slide 4: Timing Attacks
In which we analyse the time taken for a system to execute certain tasks (e.g. encryption, decryption or password entry) to reveal information leakage.

## Slide 5: Timing Attacks (Demo)
Source Code based on: http://eax64.github.io/2015/04/10/timing-attack-on-arduino.html
Removed due to large file size. The mp4 video can be downloaded from:
https://www.dropbox.com/s/906p8pwt0ksp8kk/timingattack.mp4?dl=0

## Slide 6: Timing Attack - How did it work?
The timing attack shown works due to this code within the ‘pin entry system’:
int check(char *input)
{
int i;
for (i = 0 ; i < 4 ; i++)
if (input[i] != password[i])
return 0;
return 1;
}
Each character in the input is verified consecutively leading this code to be vulnerable to timing attacks.

## Slide 7: Power Analysis
Correlate the level of power consumption to operations of the device under attack.

## Slide 8: Categories of Power Analysis Attacks
Three Main Categories:
Simple Power Analysis (SPA)
Differential Power Analysis (DPA)
Correlation Power Analysis (CPA)

## Slide 9: Simple Power Analysis (SPA)
Visual Interpretation of power traces.
Chart: Power (Volt)
10 Rounds of AES-128
1 2 3 4 5 6 7 8 9 10

## Slide 10: Differential Power Analysis (DPA)
Detect small variations in power traces based on output of cryptographic operations.
Example: output 1101 vs 1100 will produce different power consumption levels.
LSB 1
LSB 0
Source: P. Kocher, J. Jaffe, B. Jun, and P. Rohatgi, “Introduction to differential power analysis,” J. Cryptogr. Eng., vol. 1, no. 1, pp. 5–27, 2011.

## Slide 11: Correlation Power Analysis (CPA)
Correlate actual power traces against hypothesised power model.
Example: for secret key guess 65, can compare our hypothesised power model against the actual power result:
Chart: Actual Power Result for key 65
 | 4.15 | 4.15 | 4.2 | 4.21 | 4.24 | 4.25 | 4.26 | 4.3 | 4.31 | 4.29
Chart: Hypothesised Power Model for key 65
 | 4.14 | 4.16 | 4.19 | 4.22 | 4.239 | 4.248 | 4.259 | 4.3 | 4.3 | 4.2889

## Slide 12: Attacking the AES-128 S-Box running on an Arduino Uno
The experimental setup used for attacking AES-128 is shown below:

## Slide 13: Photo of Probe Setup

## Slide 14: 1-Byte Cipher Key Result using DPA (AES-128)

## Slide 15: 1-Byte Cipher Key Result using CPA (AES-128)

## Slide 16: 16-Byte Cipher Key Result using DPA (AES-128)

## Slide 17: 16-Byte Cipher Key Result using CPA (AES-128)

## Slide 18: Current Work (in progress)
Building the work of OWASP, GSMA and others,
we wish to investigate the possibility of producing a
methodology to enable us to evaluate how ‘secure’
an IoT device is.

## Slide 19: References
O. Lo, W.J. Buchanan, D Carson, “Power Analysis Attacks on the AES-128 S-box using DPA and CPA”, J. Cyber Security Technology, 2016.
Kocher P, Jaffe J, Jun B. Differential power analysis. In: Wiener M, editor. Advances in cryptology - CRYPTO’ 99: 19th annual international cryptology conference; Aug 15–19; Santa Barbara (CA). Berlin: Springer; 1999. p. 388–397.
Zhou Y, Feng D. Side-channel attacks: ten years after its publication and the impacts on cryptographic module security testing [Internet]. Cryptology ePrint archive. 2005 [cited 2016 Sep 6]. Available from: https://eprint.iacr.org/2005/388.pdf
Brier E, Clavier C, Olivier F. Correlation power analysis with a leakage model. Cryptogr Hardw Embed Syst. 2004;3156:16–29.
Pub NF. 197: advanced encryption standard (AES). Fed Inf Process Stand Publ. 2001;197:441– 311.
http://eax64.github.io/2015/04/10/timing-attack-on-arduino.html