## Slide 1: Hush Smart Baby Monitor Exploit
Ross Heenan
Abertay University - Division of Cyber Security

## Slide 2
Hush Smart Baby Monitor
The Hush Smart Baby Monitor is an IP camera that allow connection locally and remotely to monitor
Security Concerns & Threats to devices include existing and emerging one concerning new technologies
Vulnerability in device that allows an attacker to gain unauthorised access, control of device and to further escalate exploit
Ability to Locally and remotely exploit
Overview of exploit will be provided (PoC)
Exploit execution process

## Slide 3
Prerequistes
Windows 7 or Linux machine
Hush Smart Baby Monitor
Nmap scanner
Wireshark
Apktool or Java Decompilers
Steps required to carry out exploit
Enumeration of target device
Enumeration of target accompanying software
Exploitation of vulnerability
Escalation of exploit
Overview

## Slide 4
Enumeration
Target device enumeration
First step was to connect the camera to network and discover the devices network identity
(IP and MAC addresses)
nmap -sn 10.0.0.*
Returned an unknown manufacturer device with IP address
10.0.0.100
Port Scanning of discovered host
nmap 10.0.0.10x -p 1-65535
Showed TCP port 14987 open

## Slide 5
Software Analysis
Management application (Android and iOS)
Analysis of Hush Viewer v1.4.
Analysis of source code?
Apktool, Java Decompilers
Decompiling of apk application file
apktool d NameOfApk –o OutputDir
apktool d Hushviewer.apk -o Decompiled

## Slide 6
Files extracted from decompiling apk are source
Structure can be analysed for clues
Searching source code
Grep, vim, nano, text editors(gedit, notepad++), scripts
Searchwords
User, password, pwd, http, ftp, ssh….
/net/reecam/ipc
Example
Internal.java ( or .smali files)
grep user internal\$9.smali
Source code analysis
Notes: videostream.cgi get_wifi_scan_results.cgi get_misc.cgi get_log.cgi

## Slide 7
Testing vulnerability
Network identity discovered from nmap scans
IP address: 10.0.0.100
Open Port: 14987
Entered in browser presents Hush Monitor log in page
Details found to test authentication
Username: Hush17689
Password: 4bnxKRaM25
int

## Slide 8
Testing vulnerability
Wireshark
Test behaviour of device and application network behaviour
Log in while capturing
Analyse Capture
GET request shows passed in plain text over http
Successful access to interface

## Slide 9
Escalation of vulnerability
Access to all areas of admin panel
Device Status, Live Video, Device Management
Device Management Section
User Settings, Network, Wireless, DDNS, Mail, FTP, Alarm etc….
DDNS Service Settings
Remote Access

## Slide 10
Escalation of vulnerability
DDNS Service Settings
Remote Access
DDNS User Name
Serial of device

## Slide 11
Escalation of vulnerability
Camera can be accessed externally via DDNS using
http://8122h153.seecamera.info:14987
Possibility to brute force remote access
Random generation of two set of numbers
One 4 digit within a range
One 3 digit within a range
One Character
Append numbers either side of character
Access to many cameras using hardcoded credentials to access admin panel!!!

## Slide 12
Escalation of vulnerability
Spying
Locking out user
Malicious modification (FTP, Mail, Alarm)
Corruption (Factory reset, modifying firmware)

## Slide 13
http://2868h153.seecamera.info:14987/videostream.cgi?user=hush17689&pwd=4bnxKRaM25
http://192.168.0.20:14987/videostream.cgi?user=hush17689&pwd=4bnxKRaM25

## Slide 14
Compromising other devices
Devices can be generic
Same hardware
Manufacturer
Software
Insecure coding practices
Hardware access (UART)